## Slide 1: Closed-Circuit Rebreather Diver Course
Hammerhead CCR
Jeff Johnson
Et el

## Slide 2: Prerequisites
Minimum 18 years of age
Certified IANTD Advanced Nitrox Diver or Advanced Recreational Trimix
  (may be taken in conjunction), or equivalent

## Slide 3: Certification Limitations
Diver qualified on specific rebreather
  Hammerhead Closed Circuit Rebreather
Diver qualified within the sport diving depth and time limits
  Depth 140 fsw (42 msw) for Advanced EANx qualified
  Depth 160 fsw (48 msw) for Advanced Recreational Trimix qualified
  Decompression stop time not greater than 15 minutes
Training is purchased, certification is earned

## Slide 4: Program Content
Minimum 500 minutes of confined and open water dive time
At least 1 confined water & 6 open water dives
  Divers crossing over from SCR to CCR with 20 dives on SCR 400 minutes of confined and open water time and 4 dives
  From one CCR to another lectures on operating system, confined water plus 2 dives if Normoxic Trimix, Trimix, Cave or Wreck 2 additional dives at highest level of training
Two dives deeper than 50 ft (15 m)
Two dives deeper than 100 ft (27 m)
Hammerhead CCR specific exam
  Minimum score of 80%

## Slide 5: Equipment
Hammerhead Closed Circuit Rebreather
  Required Open circuit bail-out capability (on board or off board {or stage})
  Bailout cylinder for dives deeper than 90 feet (27 meters)
  Bailout cylinder (stage) on at least 3 dives
Exposure suit suitable for the environment
Back up dive tables
Slate and pencil
Reel and marker buoy
Depth gauge and timer
Knife, Z-cutter or shears
Mask and fins

## Slide 6: Closed Circuit Mixed Gas Rebreathers
Gas mixed electronically
Virtually unlimited depth capabilities
Very efficient gas supply usage
PO2 setpoint or continuos oxygen flow
Less expensive to dive especially when used with helium based gases

## Slide 7: Closed Circuit Rebreathers & Partial Pressures
Electronic control system maintains constant PO2 setpoint
Oxygen sensors detect PO2 drop & trigger solenoid valve to inject additional oxygen
Remainder of gas in loop is the Diluent which could consist of one or more inert gases

## Slide 8: Rebreather History
Early and Recent History

## Slide 9: The British Influence….. Semi- closed Circuit Rebreathers
1878
1914

## Slide 10: The German Influence…... Closed Circuit Rebreathers
1911-14
1941 - 54

## Slide 11: Commercial & Scientific Use
In the 60's and 70's rebreathers are increasingly used for commercial saturation bail-out systems.

## Slide 12: Early History
17th Century - First conceived by Giovanni Borelli
1878 - First practical system produced by Henry Fleuss
1881 - First CO2 absorbent used by Khotinsky and Lake
Prior to WWI - Dräger produced systems
WWII - Italian & British Navies used Oxygen and Nitrox systems

## Slide 13: Recent History
1969 - Electrolung - first practical electronic control Rebreather
Biomarine CCR1000, Carleton Technologies Mk 15/16
Dräger Atlantis 1 1995, Dräger Dolphin in 1998 & DrägerRay in 1999
Cis-Lunar, Inspiration, CCR 2000, Megaladon, Prism Topaz, O2ptima & Evolution
Robust & affordable systems are now available

## Slide 14: Re-circulating Scuba
Gas supply
Gas control mechanism
Counterlung
Carbon Dioxide removal system
Bail-out system

## Slide 15: Rules For Safe CCR Diving
Avoid complacency
2 Avoid distraction
3. Be a disciplined dive
4. Be a thinking diver
5. As the slogan goes always know your PO2
6. Do not be cheap
7. Make the CCR your primary diving equipment.
8. Practice bailout options periodically
  Assume any mechanical or electrical device will fail
9. Accept all emergencies taught during training will happen
10. Do not start dives with a known system failure

## Slide 16: Hammerhead CCR

## Slide 17: Hammerhead Technical Data
7.5 + lbs CO2 absorbent canister
Counterlungs 5 liter each
Weight: approx 80 lbs. with 3 L steel cylinders;
Two or more cylinders: Sizes can be interchanged for mission.
ADV (Automatic Diluent Valve)
One oxygen control units (primary display)
One oxygen partial pressure monitor (secondary display) HUD
Decompression included in primary can be added to secondary

## Slide 18: Hammerhead Safety Features
Water traps in loop
  In base of scrubber canister
  Exhalation counter lung
Dual independent electronics
  Primary and secondary independent of each other
10 hours plus battery life duration
Sensor diagnostics
ADV in inhalation counter lung
HUD
Real Time Decompression Computer

## Slide 19: Hammerhead Safety Features
Solenoid fires even if in OC if PO2 drops below 0.19
  Firing rate is adjustable
Shallow water auto 0.4 set point
One primary O2 Display
  Controls solenoid, and reads PO2 in the loop
  Primary tracks depth and run time and decompression
  Easy to use and set up menu
One secondary display
Displays have independent calibrations and independent systems isolated from each other

## Slide 20: Hammerhead Power On
Systems powers up by multiple means for safety:
  Touching Piezo selector button
  Alternatively by wet switch
  Or by pressure sensor upon reaching 1 meter
  Unit will go into sleep mode after 2-30 minutes
  HUD turns on with secondary electronics
The O2 controller take readings from the 3- O2 cells
Voting Logic
  The Master averages the 3 cells and discards the out of range cell
  Solenoid matches the selected set point
Solenoid , highly energy efficient

## Slide 21: Hammerhead Oxygen Controller/ Primary Display
The O2 controller take readings from the 3- O2 cells
Solenoid , highly energy efficient
Placement of solenoid ejection point ensures gas mixed prior to inhalation side of loop
Primary has it’s own independent power supply

## Slide 22: Hammerhead Display
Easy to follow menu
  Display has two push buttons one for menu scroll, select and confirm
    The left button scrolls through the selections available
    Right button “selects”
    Once a selection is to be used touch the left button to confirm

## Slide 23: Primary continued
Primary selections
  5 set points pre set and changed in the options menu
  Those 5 set points can then be selected from the main screen
  Gas selection based on pre-selected gases in options menu
  up to 10 gases can be preprogrammed
  FO 2 mode
  OC mode for bailout decompression status
  If you go OC you must change this setting for decompression accuracy

## Slide 24: Primary Options
Options menu
  Select gas allows user to program gases in
  Decompression conservatism/Gradient Factor
  Be conservative with GF compare to computer you are accustomed to diving 35/70 is the most conservative setting
  - Custom Gradient: use with care, always error to safety
  Define Set point selection features:
    User defined set points between .4 and 1.6

## Slide 25: O2ptima Primary Display
Options menu continued
  Calibrate O2
  Back light time
  Imperial or metric use
  Solenoid firing rate (Juergensen, Standard, Manual (OFF!)
  Auto Shutdown rate ( 2-30 minutes)
  MV display
  Barometer
  Standard error

## Slide 26: Hammerhead Primary Display
Options menu continued
-Password MGR
-Go to Sleep
- BS - O - Meter
- About
- Diagnostic PSWD
- Exit

## Slide 27: Hammerhead Secondary PO2 Display
The secondary display simply displays the PO2 calculated from its own readings of the oxygen cells
The secondary calibration is independent of the primary
  The HUD is calibrated with the secondary
Secondary has its own independent power supply
Decompression can be added to secondary
Unlock code must be purchased
Gases must be loaded and selected
Gradient factor must be selected

## Slide 28: Hammerhead Secondary
Power failure occurs on primary
  PO2 may be monitored on the secondary display and unit dived manually to exit water safely
  Utilizes appropriate PO2 table
  User scrolls to the setpoint that has been selected and verifies PO2

## Slide 29: Hammerhead Heads up display
Display gives alert message, red warning light and diva vibrator activates if set point varies 0.2 from selected set point
Green led flashes every 8 seconds and “ok” on screen
when sensor readings are within 15% of set point
Yellow led flashes every 5 seconds and “warning” on screen
when readings are 15% - 24% out of range
a sensor has been voted out
Red led flashes every 2 seconds when sensor 25% or more off setpoint
PO is = to or less than .19
PO is = to or greater than 1.8
Vibrator in Diva will activate
Back light on wrist unit will flash

## Slide 30: Hammerhead Secondary PO2 Display
Options permitted by diver in menu:
  Define set point - Barometer
  Calibrate O2 - Set Diva mode
  Stack Timer Options - MV Display
  Back light timer - BS-O-Meter
  Imperial Metric - About
  Auto shutdown - Diagnostic PSWD
  Display Options - Exit
  Password Manager

## Slide 31: Hammerhead secondary continued
There are 3 screen display modes available
Classic
Displays system status, PO2 and warnings on single screen
Depth and Timer Displays on 3 alternating screen
1st screen is classic mode
2nd screen current depth, temp and max depth
3rd screen current depth and dive time
PO2 is displayed in the second line on every screen
Depth, Timer and Stack Time 4 alternating screens
1st three screens are identical to Depth Timer mode
4th screen is stack time used, timer begins once diver submerges

## Slide 32: Hammerhead stack timer
Programmable limit set by diver in options
Alarm when exceeded
A negative time will be displayed
Back light will flash
“stack over run” will be displayed
Diva will flash red / green, red / green
Vibrator in diva will activate twice
Warning will repeat every 2 minutes until cleared by
reprogramming stack time

## Slide 33: Hammerhead Calibration
Turn power on
Scroll through both hand sets to calibration menu
Calibrate primary then secondary
  Menu will state fill loop with oxygen
    From a negative fill loop complete with oxygen
    Breathe down refill with oxygen
    Repeat minimum of 3 times (minimum)
    Hit select button unit will calibrate or indicate it failed to calibrate and why
If unit fails calibrate it will signal alert, give red light and the mouthpiece vibrator will activate

## Slide 34: Hammerhead Oxygen Cells
The Hammer Head uses the R 22 D Teledyne sensor
  Voltage is from 8 to 13 m volts
Because of this variation and the cell’s output reduces with age, it is necessary to verify calibration or calibrate prior to each days use
Calibration is extremely easy, taking 3 flushes of the unit and is performed on the assembled unit

## Slide 35: Electrical Oxygen Sensors
Critical components - redundancy
Galvanic fuel cells
Lead anode - gold plated cathode - Potassium Hydroxide solution
Lead is oxidized producing small voltage between anode & cathode
Individually calibrated
Affected by humidity and temperature

## Slide 36: Interpreting PO2 Display
The PO2’s from the 3 Oxygen Cells are the most important data you have to monitor
Do It Regularly!
Compare the PO2 displays to each other and to setpoint
Note the speed at which the PO2 readings change
  A slow reacting cell probably indicates moisture on that cell’s sensing face

## Slide 37: Controlling Setpoint on the Hammerhead
Select set points in user programmable menu in options set up
  Program from .4 to 1.6
  Any 5 set points may be programmed
Changing set points
  Setpoints can be changed any time
  Simply scroll through set points with left button and select setpoint
  Select with right button
  Confirm with left button

## Slide 38: Cylinder Considerations
BCD & drysuit inflation gas will affect Rebreather duration
Diluent used primarily during descents
Oxygen is more likely to limit dive duration

## Slide 39: The Counterlung
Necessary for free breathing
  Empty bottle vs. paper bag
Constant Buoyancy
  Exhale: lung volume decreased & bag volume increases
  Inhale: lung volume increases & bag volume decreases
  Compare to Open Circuit Scuba
Position to minimize pressure differential between lungs and counterlung

## Slide 40: Hydrostatic Effect
Chest mounted bag - diver horizontal
  Inhale less effort
  Exhale more effort
Back mounted bag - diver horizontal
  Inhale more effort
  Exhale less effort
Shoulder mounted bags - most positions
  Inhale & exhale equal effort

## Slide 41: Breathing Loop
Scrubber for CO2 Removal
  Exhaled gas passes through this for “filtering effect”
  Efficiency and work of breathing is related to size / types of granules
  Temperature sensitive
  Design also effects the efficiency

## Slide 42: Absorbent Canister Design
Gas exposed to sufficient surface area of absorbent to remove CO2
Gas flow rate across absorbent sufficient time (dwell time) for chemical removal of CO2
Simple & correct packing to prevent ‘channeling’ of absorbent
Prevent excess moisture from reaching absorbent

## Slide 43: Absorbent Canister
Radial Flow System - gas flows through ‘block’ of absorbent in radial fashion. Flows from exterior to interior center tube which connects to inhalation side of the loop.

## Slide 44: Absorbent Canister
Radial Flow System - gas enters center of ‘doughnut’ cross section & radiates outwards through the absorbent (or from the outside inwards)

## Slide 45: Absorbent* Types
All Absorbents will Produce a Caustic Effect if Mixed with Water
Barium Hydroxide - the earliest form of absorbent used
Lithium Hydroxide - long lasting and efficient, but must be carefully handled and is expensive
Soda Lime - a commonly used absorbent available under trade names such as Sofnolime™ and Dräger Divesorb®

## Slide 46: Carbon Dioxide Absorption
Typical diving grade soda lime absorbent
  94% Calcium Hydroxide [Ca(OH)2]
  4% Sodium Hydroxide [NaOH]
  1% Potassium Hydroxide [KOH]
  <1% Silica (binding agent)
Some types change color with use
Slightly hydrated to ensure production of Carbonic Acid

## Slide 47
CO2 reacts with water (vapor) to form weak Carbonic Acid
Carbonic Acid reacts with base to produce salt (chalk), water & heat
CO2 + H2O  H2CO3
H2CO3 + 2NaOH  Na2CO3 + 2H2O + Heat
H2CO3 + Ca(OH)2  CaCO3 + 2H2O + Heat
Carbon Dioxide Absorption

## Slide 48
Reaction of carbon dioxide with soda lime produces calcium carbonate
Credit: Chris Switzer

## Slide 49
Reaction of carbon dioxide with soda lime produces heat (exothermic reaction)
Credit: Chris Switzer

## Slide 50
NaOH and KOH are needed along with the major scrubber component of Ca(OH)2 in CO2 absorbent to promote fast and efficient reaction with carbon dioxide and carbonic acid in the scrubber. The reason is that NaOH and KOH are more reactive and more soluble than Ca(OH)2.
Absorbent composed of Ca(OH)2 alone is produced for medical applications under the trade name of Amsorb®. The carbon dioxide absorption capacity of Amsorb® has been reported as being as little as half that of soda lime.* This illustrates the importance of NaOH and KOH in small quantities along with Ca(OH)2 in absorbents, and the need to only use absorbents designed and approved for diving.
*Higuchi, H., et al., International Anesthesia Research Society, 2001, 23, 221.
**Collins, V. J. “Principles of Anesthesiology,” 1976, Lea & Febiger, Philadelphia, PA.
Another key absorbent parameter is water content. Although water is needed to react with carbon dioxide to produce carbonic acid, some of the water in the absorbent is used to counteract the heat of the scrubber reaction by vaporization. If too much water is present, absorbent pores will fill and reduce the surface area available for reaction. Too little water and the absorbent dries out, shortening its life.**
Absorbent facts -- the need for minor hydroxide components and water
Credit: Chris Switzer

## Slide 51: CO2 Absorbent Duration Variables
Chemical composition
Canister volume
Temperature
Exertion level
Moisture level

## Slide 52: CO2 Absorbent Materials
The Hammerhead CCR is being tested by the Micropore facility
Until final testing limit dives to manufacturers present recommended limits

## Slide 53: Packing Hammerhead Absorbent Canister
Using a loose fill scrubber material
  Remove old scrubber material
  Dispose of according to mfg guidelines
  Clean sidewalls, O rings
  Inspect Scrubbing Canister including o-rings
  Fill no more than 1/3rd and tamp
  Fill no more than 2/3rd and tamp
  Fill to proper level and tamp
  Upon completion lay on side and tamp circumference to even pack from tighter / loose layering so that radial channeling does not occur

## Slide 54: Face Masks
Rebreathers have limited gas supply
Proper fitting mask to prevent leaks
Repeated mask clearing depletes gas supply
Full face mask allows U/W communications
  Full face should be low volume to prevent CO2 build-up and avoid gas loss

## Slide 55: Breathing Characteristics
More natural breathing than Open Circuit
Breathing resistance depends on location of counterlung and diver’s body position
Water in loop increases breathing resistance
Humid gas reduces dehydration of diver
Warm gas reduces heat loss from diver
Both effects should reduce the risk of DCS

## Slide 56
Hammerhead Pre-Dive
Analyze gas in cylinders, & check pressures
  Diluent cylinder
  Oxygen cylinder
  Bail-out cylinder (s)
Inspect parts and electrical connections for dirt, deterioration, solid connections, and damage
Lubricate where applicable
Record accumulated time on absorbent, replace as needed
Check non return valves in DSV (Dive Surface Valve)

## Slide 57: Hammerhead Pre-Dive Checks
Assemble unit (install canister, lid, Breathing loop, Regulators, oxygen OD, manual oxygen, adv, harness ensure lid seals, etc.)
Verify solenoid operation
Verify Display on the primary and secondary
Attach displays to cylinders for protection
Pressure checks
Positive pressure check
Negative pressure check
Cylinder pressure leak checks
Open oxygen and Diluent supply gas valves
Verify oxygen and Diluent by pass valves
Verify ADV (if applicable)

## Slide 58: Pre-dive Pre-Dive Checks
Record cylinder pressures
Turn valves off verify no leak after 2 minutes
Calibrate primary
Calibrate secondary
Check setpoint maintenance
Verify 0.4 maintained
Verify 0.7 maintained
Ensure system will lock into all set points
Pre dive breathe
At a low set point breathe 2 minutes (5 minutes cold water)
Verify diluent addition
Verify safe PO2 prior to entering water

## Slide 59: Hammerhead Pre-Breathe Sequence
Pre-breathe 2 - 5 minutes
  Open mouthpiece (DSV) and breathe normally
  Have low setpoint (0.4) selected
  Confirm oxygen controller maintains PO2 setpoint
  Operate Diluent and oxygen manual addition valves
  Confirm CO2 absorbent functioning correctly
  Confirm BCD inflation and deflation
  Confirm bail-out system operation
  Confirm ADV operation
  Confirm cylinders on

## Slide 60: Dive Procedures
Initial in-water verification
Descent - diluent addition
Buoyancy control
Monitoring PO2
Minimum loop volume
Monitoring gas supplies
Ascents

## Slide 61: HH CCR Initial In-Water Verification
Check for leaks
Verify Primary O2 control system working
Verify Secondary PO2 display working
Adjust buoyancy
Check your dive buddy

## Slide 62: Descents
Counterlung collapses as ambient pressure increases
  Add diluent to maintain breathing volume
Compensation by diluent gas addition
Rapid descents cause PO2 spikes
Select Low PO2 setpoint for descent
  As ambient pressure increases so will the PO2
Switch to High PO2 setpoint at target depth

## Slide 63: Buoyancy Control
No buoyancy changes during breathing cycle
  Except for oxygen metabolised
Buoyancy adjustments using lung volume therefore not feasible
Counterlung collapses during descent & expands during ascent
Buoyancy change from fully collapsed to fully inflated is considerable

## Slide 64: Hammerhead Monitoring PO2
Constant PO2 Monitoring is Vital
Check every 1 to 4 minutes
Hypoxia & Hyperoxia are real dangers
Frequent cross checking of both primary & secondary

## Slide 65: Monitoring Gas Supplies
Gas supplies used at much slower rate than OC but monitoring is still necessary
Small gas supply quickly used if there are leaks in the loop, frequent mask clearing or frequent ascents / descents
O2 supply not diluent supply, typically limits duration of dive

## Slide 66: Hammerhead Ascents
Buoyancy changes due to expansion of the counterlung, BCD and drysuit
PO2 should not be allowed to drop
The Hammerhead will attempt to maintain the setpoint on ascent
Oxygen can be manually added if necessary

## Slide 67: Physiological Concerns
Hypoxia (O2 deficiency)
Hyperoxia (CNS O2 toxicity)
Hypercapnia (CO2 toxicity)
Decompression Sickness
Chemical Injury
Hypoxia, Hyperoxia & Hypercapnia may cause Loss of Consciousness with little or No warning!

## Slide 68: Failure Modes
Bail-out Scenarios
  Hypoxia
  Hyperoxia
  Hypercapnia
  Solenoid failures
  Complete electronics failure
    Semi-closed mode
    Minimum loop volume
In an Emergency - Poorly Learned Survival Skills Are Lost First

## Slide 69: Hypoxia
Lack of oxygen at cellular level
  First signs at PO2 of 0.16 Serious signs PO2 of 0.10
Lack of coordination
  Confusion
  Euphoria
  Inability to think clearly
  Unconsciousness & death
Switch to Open Circuit for one or more sanity breaths
Switch back to Rebreather
Diluent flush
Check PO2
Repeat until PO2 setpoint is obtained
If PO2 Remains Low,Switch to
Open Circuit & Bail-Out
Hypoxia Can Lead to Unconsciousness & Death Without Warning

## Slide 70: Problems that lead to Hypoxia
Failure to turn oxygen on
Oxygen solenoid feed line not connected
Wrong gas in oxygen cylinder
Failure to calibrate
Failure to do pre dive Breathe and checks
Failure to monitor PO2
Running out of oxygen supply gas
Solenoid fails in shut position
Mistakes Due To Complacency or Distraction = Accidents or Death

## Slide 71: Solenoid Failure - Closed Diver Chooses To Continue Diving Rebreather
If the PO2 reads below the Diluent PO2, or if it is approaching a a PO2 below 0.3 ATA. Switch to Open-Circuit for sanity breaths
Switch back to Rebreather and flush the loop
Manually add O2 via Manual Addition Valve
Check PO2
Manually add O2 as needed to maintain setpoint
IANTD Recommends Open Circuit Bail-Out

## Slide 72: Hyperoxia
Excess of oxygen at cellular level
PO2 of 0.5 to 1.0 ATA/Bar
  Whole Body Oxygen Toxicity
PO2 > 1.0 ATA/Bar
  CNS Oxygen Toxicity
Convulsions underwater may result in drowning
Switch to Open-Circuit for
one or more sanity breaths
Switch back to Rebreather
Diluent flush
Check PO2
Repeat until PO2 setpoint is obtained
If PO2 Remains high,Switch to
Open Circuit & Bail-Out
Hyperoxia Can Lead to Convulsion & Drowning Without Warning

## Slide 73: CNS Oxygen Toxicity
PO2 > 1.0 ATA/Bar
CON - Convulsions
V - Vision
E - Ears, hearing disturbances
N - Nausea
T - Twitching
I - Irritability
D - Dizziness

## Slide 74: Tracking O2 Limits
CNS tracking couldn’t be simpler
Use the IANTD O2 exposure table, at 1.3 ATA you have 3 hours dive time or 3.5 hours per day
Remember, if you push the PO2 up to 1.4 ATA the dive time is reduced to 2.5 hours or 3 hours per day
Refer to IANTD OTU /CNS Tracking Table C 3201 in the student kit to determine exact oxygen exposure
Then for repetitive CNS value use the oxygen surface credit chart

## Slide 75: Problems that lead to Hyperoxia
To high of oxygen percentage in Diluent
Oxygen leaking through schrader valve
Rapid descent started with to high of a setpoint
Adding oxygen during descent
Set point maintained to high for dive duration thus exceeding oxygen clock
Failure to calibrate unit
Solenoid fails in open position

## Slide 76: Solenoid Failure - Open Diver Chooses To Continue Diving Rebreather
IANTD Recommends Open Circuit Bail-Out
Switch to Open Circuit for sanity breaths
Close oxygen supply cylinder valve
Switch back to rebreather
Diluent flush, check PO2
Open and close O2 supply cylinder as needed to maintain set point
  If problem is leaking schrader valve disconnect inflator hose

## Slide 77: Hypercapnia
PCO2
  0.03 ATA/Bar - doubles breathing rate (dyspnea)
  0.06 ATA/Bar - distress, confusion, lack of coordination
  0.10 ATA/Bar - severe mental impairment
  0. 12 ATA/Bar - loss of consciousness, death
Bailout to OC
  Go to manual mode or a low set point or OC mode to avoid solenoid injecting oxygen and increasing buoyancy
  Disable ADV to avoid
  Remain off loop
Ascend
Hypercapnia Can Lead to Unconsciousness & Death Without Warning
o

## Slide 78: Problems that Lead to Hypercapnia
Using canister beyond it’s rated /actual duration
Over breathing the canister capability to keep up with
Wrong material
Using absorbent that has exceed it’s expiration date
Absorbent is wet
Deep diving on partially used canister

## Slide 79: CO2 Absorbent Problems
Switch to Open Circuit Bail-Out
Switch to Open Circuit Bail-Out
Flooded Canister
  CO2 absorption falls, caustic cocktail in loop
Absorbent Failure
  CO2 absorption falls

## Slide 80: Moisture In Loop
Roll Right, Down and Then Up While Exhaling
Always some moisture due to condensation
Accidental removal of mouthpiece
Move water into exhale counterlung

## Slide 81: Water In Loop
Switch to Open Circuit Bail-Out
Leaky hose connections, damaged hoses, punctured counterlung & other damaged loop components
Gurgling sound & breathing resistance
Decrease in buoyancy
Clear flooded loop
If problem continues

## Slide 82: Asphyxia
If diver breathes in and out of a closed bag
  CO2 rises and O2 falls
Dyspnea - increasing shortness of breath
Breathing difficulties caused by increased CO2
Death caused by insufficient O2

## Slide 83: Complete Electronics Failure Extreme Emergency Diver Chooses To Continue Diving Rebreather
IANTD Recommends Open Circuit Bail-Out
With proper training diver has three options
  Open Circuit bail-out
  Semi-Closed mode
  Minimum Loop Volume

## Slide 84: Semi-Closed Mode Extreme Emergency Diver Chooses To Continue Diving Rebreather
Diver must be trained how to use this technique before attempting this procedure in an emergency situation
Switch to Open Circuit for sanity breaths
Switch back to rebreather, Diluent flush
Exhale out of loop via mouth or nose every 3 - 5 breaths
Diluent flush prior to ascent
IANTD Recommends Open Circuit Bail-Out

## Slide 85: Minimum Loop Volume Diver Chooses To Continue Diving Rebreather
Diver must be trained how to dive Rebreather manually before attempting this procedure
  Loop volume just enough for a single normal breath
  Extra volume is wasted gas and added buoyancy
  PO2 stays close to setpoint
Maintain constant loop volume by manual oxygen addition
Maintain constant depth, do not descend or ascend
SCR mode for ascent to 20 fsw (6 msw), then add oxygen to maintain loop volume
IANTD Recommends Open Circuit Bail-Out

## Slide 86: Basic Respiratory Physiology
21% oxygen in air at sea level
4% absorbed into blood
  Exhaled air contains approximately 17% O2
Urge to breathe is triggered by PCO2
Respiratory rate determined by rate of CO2 production

## Slide 87: Basic Respiratory Physiology
Respiratory minute volume (RMV) = total gas ventilated in one minute
  RMV determined by respiratory rate & volume of gas ventilated each breath
OC duration determined by RMV
SCR duration determined by flow rate
CCR duration determined by O2 metabolic rate

## Slide 88: Oxygen Metabolism
Oxygen Consumption Varies With Work Load
  At rest ------------------------ 0.3 - 0.5 L/min
  Light to moderate work ----- 1.0 - 1.5 L/min
  Heavy work ------------------ 2.0 - 2.5 L/min
  Maximum work -------------- 3.0 - 3.5 L/min
Increase Gas Efficiency by Rebreathing It!

## Slide 89: Gas Consumption Comparison
Absolute Open Closed
Depth Pressure Circuit Circuit
fsw (msw) ATA/Bar lpm lpm
0 (0) 1.0 25 1
33 (10) 2.0 50 1
66 (20) 3.0 75 1
99 (30) 4.0 100 1
132 (40) 5.0 125 1
165 (50) 6.0 150 1
231 (70) 8.0 200 1
297 (90) 10.0 250 1

## Slide 90: Closed Circuit Oxygen Metabolism
O2 supply = 3 liters @ 200 Bar = 600 litres
Metabolic rate = 1.0 lpm @ moderate work load
Assumes no leakage from mask or loop - Duration independent of depth

## Slide 91: Open Circuit Gas Usage
HH CCR: 3 litres at 200 Bar = 600 litres
Open Circuit Equipment:
RMV at surface = 20 lpm
RMV at 66 fsw (20 msw) = 60 lpm
600 litres/60 litres per minute = 10 hours
10 min Open Circuit =
10hours Hammer Head

## Slide 92: Bailout On OC at 30 meters (100 feet)
Diver breaths 20 L min (0.66 ft3 ) on the surface
Due to increased RMV under Stress we will use the 30 m (100 ft) RMV for this example
  At depth the diver breathes 80 L min (2.64 ft3 )
  Bailout is on a 3 L cylinder (20 ft3 )
  It will take approximately 1 minute for the diver to calm down once on OC then 3 minutes to ascend and a 3 minute safety stop - Total time on OC 7 minutes
  this is 560 L to make the ascent (18.48 ft3 )
Would you consider a partially used 3 L (20 ft3 ) cylinder acceptable for bailout

## Slide 93: Rebreathers & Decompression
Partial pressure of inert gas determines decompression obligation
Open Circuit & Semi-Closed Circuit - PO2 maximum only at target depth
With Closed Circuit constant PO2 (setpoint) increases decompression efficiency
  Some units can modify setpoint during the dive
Dramatically reduces decompression obligation

## Slide 94: Decompression Efficiency
The most efficient is Closed Circuit Rebreather
The second most efficient is EANx or Trimix Open Circuit
The third is Semi-Closed Rebreather
The least efficient is Air Open Circuit
CCR is the ideal system for decompression efficiency and ease of oxygen tracking

## Slide 95: Oxygen & Inert Gas % in Breathing Gas
Depth Pressure PO2 FO2 Finert
10 fsw (3 msw) 1.3 Bar 1.3 Bar 100% 0 %
20 fsw (6 msw) 1.6 Bar 1.3 Bar 81.3% 19.7 %
33 fsw (10 msw) 2.0 Bar 1.3 Bar 65.0% 35.0 %
66 fsw (20 msw) 3.0 Bar 1.3 Bar 43.3% 56.7 %
99 fsw (30 msw) 4.0 Bar 1.3 Bar 32.5% 67.5 %
132 fsw (40 msw) 5.0 Bar 1.3 Bar 26.0% 74.0 %
165 fsw (50 msw) 6.0 Bar 1.3 Bar 21.7% 78.3 %

## Slide 96: Chemical Injury
Caustic cocktail
  May produce mild irritation to third degree chemical burns
  Some absorbents may be lethal if wet
  (Lithium Hydroxide for instance)
Battery related injuries
Electrical injury

## Slide 97: Rebreather Maintenance
Disinfecting & cleaning
O-rings
Hoses
Counterlungs

## Slide 98: Disinfecting & Cleaning
Rebreather - warm, damp environment is ideal for bacterial growth
Breathing loop regularly disinfected & dried thoroughly
Safe disinfectants only
Cleaning agents may affect O-rings
O2 compatible lubricants only

## Slide 99: After Each Day Of Diving
Vent electronics head to the atmosphere
Drain exhale counterlung
Wash mouthpiece in fresh water
Re-pack absorbent, fill cylinder as necessary

## Slide 100: Post Dive & Storage
Rinse exterior of unit
Remove/dispose absorbent
Clean scrubber canister
Rinse/disinfect breathing bags & hoses
For storage, leave cylinders partially filled
Allow unit to dry, lubricate all O-rings

## Slide 101: O-Rings
Do not disturb O-rings unnecessarily
Carefully inspect prior to reassemble
Replace damaged O-rings
Excessive lubrication not required
Check O-ring grooves for damage
O2 compatible lubricants only
Factory sealed compartments - don’t tamper

## Slide 102: Hoses
Check for visible damage after every dive
Store in hard carry case
Do not carry unit by hoses
Do not place heavy equipment on hoses

## Slide 103: Counterlungs
Keep dry (vented) when not in use
Check loop interface ports for damage to threads, etc.

## Slide 104: Summary
Always Know Your PO2
Be Sensible, Be Safe!
Advantages of Rebreathers greatly outweigh the disadvantages
Correct training is obligatory

## Slide 105: CCR Student Skills Confined Water
Preparation Checklist
  Walk students through the “Pre-Dive Check” Sequence
  Emphasize that students must work in buddy teams PRIOR TO IMMERSION
  Remind students to close the mouthpiece when switching to open circuit
Introduction to CCR
  Breathe on unit at rest
  Once comfortable swim unit to develop a feel for it

## Slide 106: CCR Student Skills Confined Water
Oral Inflation of BCD for Buoyancy Control
  Swim unit for reasonable time doing manual BCD inflation
Buoyancy Control Using BCD
  Repeat above drills using BCD with auto inflation

## Slide 107: Confined water
Buoyancy Practice
  Once buoyancy is adjusted appropriately, students should swim the unit
  Have students practice buoyancy control with use of breathing bags as backup procedure
  Use BC for buoyancy control - students maintain a stable depth at rest
  Ascend in gradual steps of approximately 1½ feet (1/2 meter) at a time maintaining a stable swim depth - At each level circle a segment of the confined water area, until the surface has been reached - Then repeat the sequence while descending
  When reasonably proficient in swimming buoyancy control students should make a gradual ascent and hover at assigned levels with a minimum of movement - Repeat at various depth increments until the surface is reached - Repeat during descent

## Slide 108: CCR Student Skills Confined Water
Acclimatization to Loop Volume and Delivery Capabilities
  Complete rapid swims to allow individuals to discover that the system provides ample gas flow
Counterlung Volume Control
  Have students swim while varying depths
  Divers should be able to maintain adequate bag volume without having to stop swimming

## Slide 109: CCR Student Skills Confined Water
Introduction to Minimum Loop (Constant Loop) Volume diving
  Demonstrate Constant Loop Volume technique as a response to a simulated complete electronics and O2 sensor loss (conduct this skill only in confined water) - Also as a means of better buoyancy control and less drag while swimming
  Procedure for Constant Loop Volume Technique: Students should in confined water establish a loop PO2 of greater than 0.5 - The PO2 should be set at 0.5 as a safety measure - The diver should establish a minimal loop volume so that on a full inhalation the counterlung is bottomed out - The diver should continually monitor the PO2 and be instructed to bail-out to open circuit if necessary
  Swim unit for a reasonable time becoming familiar with constant loop volume diving

## Slide 110: CCR Student Skills Confined Water
Technique Practice & Readjustment of Unit
  Work on dive technique and trim and continue acclimatization to the unit
  Check that system configuration is comfortable and make adjustments as needed to the harness, weights and other components
Practice OC Bailout
  Switch from CCR to OC then back, be sure to purge water out of mouth piece prior to switching into CC mode
  Repeat until proficient
  Practice skill while swimming
Emergency Drills
  Students should practice emergency procedures for dealing with hypoxia, hyperoxia and hypercapnia

## Slide 111: CCR Student Skills Confined Water
Hyperoxia Drill
  Simulation: The diver has recognized a high PO2 on display, heard an audio warning or heard a solenoid stick in the open position
  Procedure: Switch to open circuit - Inhale from open circuit - Switch to closed circuit and begin a Diluent flushing of unit - Carefully monitor the PO2 during this procedure - Breathe from closed circuit when PO2 reaches an acceptable level
  To simulate Hyperoxia drill due to failed solenoid repeat above but also turn oxygen supply gas off - Maintain PO2 by manually turning oxygen valve on and off
Simulation Drill of Failed Open Solenoid
  Establish a high setpoint and maintain a PO2 that is less than than this by control of the oxygen supply valve

## Slide 112: CCR Student Skills Confined Water
Hypoxia Drill
  Simulation: Student has recognized a low PO2
  Procedure: Switch to open circuit, check display, inhale from open circuit, switch back to close circuit and begin a Diluent flushing
  Recheck display and adjust PO2 to appropriate level by using oxygen addition valve, recheck display and continue breathing from closed circuit if appropriate
  Diver may switch to open circuit to take a breath during drill if required
Simulation Drill of a Solenoid Failed in the Closed Position
  Student is to set a low setpoint and maintain a PO2 that is above this value by manual addition of oxygen

## Slide 113: CCR Student Skills Confined Water
Hypercapnia Drill
  Simulation: Student has determined that his/her canister has broken through
  Procedure: Abort to open circuit
Loop Flooding Drills
  Demonstrate partial flood recovery
  Procedure for Partial Flood: Look up and exhale rolling exhalation hose downward
  Allow gravity to move water down to right couterlung
  Exhaust fluid through the exhaust valve on the counterlung by purging the Diluent addition valve

## Slide 114: CCR Student Skills Confined Water
Manual Control
  Practice flying unit under manual control by lowering the PO2 set point and manually maintaining a higher set point
  Monitor PO2
  Repeat buoyancy drills using manual control
  Practice flying unit manually by turning oxygen cylinder valve on and off
Semi-Closed Circuit (SCCR) Operation
  Fly unit as SCR using Diluent addition
  Exhale and do a dilluent flush every 3 to 5 breaths

## Slide 115: CCR Student Skills Confined Water
Oxygen Metabolism Exercise
  Instruct divers to adjust to a PO2 above where the setpoint is
  Monitor how long it takes for the PO2 to drop 2 points at rest (i.e. 0.7 to 0.5)
  Repeat the above exercise while swimming
Post Dive Procedures & System Clean Up

## Slide 116: CCR Student Skills Open Water Training on CCR Must Include the Following Skills
Pre-dive checks
Pre-dive breathe
Low setpoint for descent
Switch to higher setpoint once the diver is at the planned dive depth or setpoint change depth
In water leak and buddy check Where practical this may be accomplished between just below the surface to 20 fsw (6 msw) deep - If conditions prohibit this then immediately upon arrival at a stable depth
Descend and insure Diluent addition is made
Open Circuit bailout (static and dynamic) drills, including at least two OC ascents to approximately 20 fsw (6 msw)
Buoyancy and trim
Handset/computer/pendant, etc. operation
Gauge monitoring PO2 monitoring to be done no more frequently that once a minute and no less often than once every four minutes
Hypoxia (static and dynamic drills)
Hyperoxia (static and dynamic)
Hypercapnia (static and dynamic)
Flood recovery (static and dynamic)

## Slide 117: CCR Student Skills
Buoyancy and trim on the bottom, during ascent and at safety or required stops
Hypoxia due to Solenoid stuck in closed position (reset to a low setpoint and maintain a higher PO2 by manual addition (dynamic)
Hyperoxia due to Solenoid stuck in open position (reset to a high PO2 maintain at a value less than this by valve) manipulation (dynamic
Dive the unit manually
Minimum Loop Volume
Carry off-board bailout cylinder on 3 or more dives
SCR mode of diving
SMB deployment
Out-of-air, air gas sharing from OC bailout (donor remains on CC)
Complex (multi-part) scenarios such as Hypoxia or Hyperoxia drill for donor while gas sharing with a out of gas diver
Ascend
Safety or required Stop
Post dive briefing
Unit maintenance

## Slide 118
CCR Student Skills Student Reacts to Scenarios - Include on at Least 2 Dives
Inhalation counterlung inflating
Feeling unusual
Buoyancy changed to negative
Difficult breathing counterlung at correct volume
Weakness in legs
Shortness of breath
Feeling of well being
Feel like you are about to blackout
Muscle twitching
Nausea
Ears ringing
Hearing or visual abnormalities
You feel dizzy
Extreme quietness (absence of solenoid noise)
Solenoid fires but no oxygen is injected
Diluent not being added
2 cells read high but low cell checks with Diluent PO2
2 cells read high and check with Diluent PO2

## Slide 119: CCR Student Skills Recommended OW Dive Sequence
The skills are recommended to be performed as in the following 8 dive sequence
Changes in this sequence may be made by the Instructor due to environmental factors or the students performance
All skills must be completed even if in a varying order or if extra dives are required to do so

## Slide 120: CCR Student Skills On All OW Dives Skills May Be Presented in Different Order If Circumstances Dictate
Pre-dive checks
Pre-dive breathe
Leak check
Descend – Diluent addition
Handset operation
Handset and gauge monitoring
  No more than 1 minute
  No less than 4 minutes
Switch to high setpoint at planned depth
Buoyancy and trim at depth
Buoyancy and trim on ascent
Buoyancy and trim at safety stop
Post dive briefing
Unit maintenance

## Slide 121: CCR Student Skills OW Dive 1
Major emphasis on buoyancy control
Do Each of the Following Drills at Least Once
Open Circuit Bailout (static)
Hypoxia (static)
Hyperoxia (static)
Hypercapnia (static)
Flood Recovery (static)
Ascend

## Slide 122: CCR Student Skills OW Dive 2 Do Each of the Following Drills at Least Once
Open Circuit Bailout (dynamic)
Hypoxia (dynamic)
Hyperoxia (dynamic)
Hypercapnia (dynamic)
Partial flood recovery (dynamic)
Ascend slowly with good buoyancy control

## Slide 123: CCR Student Skills OW Dive 3 Do Each of the Following Drills at Least Once
Close oxygen valve monitor drop in PO2 (1.3 to 1.1) then re-open valve
Hypercapnia (dynamic)
Flood recovery (dynamic)
Solenoid stuck in closed position (reset low setpoint to 0.5 and manual addition to maintain desired setpoint) (dynamic)
Solenoid stuck in open position setpoint at 1.3, maintain 1.1 via oxygen valve (dynamic)
Open Circuit bailout (dynamic)
Ascend
Safety Stop (dynamic stop without holding onto ascent line)

## Slide 124: CCR Student Skills OW Dive 4 Do Each of the Following Drills at Least Once
Minimum Loop Volume
Hypoxia (dynamic)
Hyperoxia (dynamic)
Hypercapnia (dynamic)
Flood recovery (dynamic)
Solenoid failure in the closed position (change setpoint to 0.5 and use manual oxygen addition to maintain desired setpoint)
Solenoid failure in the open position (reset setpoint to 1.3, maintain 1.1 via oxygen valve) (dynamic)
Out of gas (gas sharing by using buddies stage and hand-off of stage)
Ascend (open circuit bailout to safety stop)
Safety Stop (on CCR)

## Slide 125: CCR Student Skills OW Dive 5 Do Each of the Following Drills at Least Once
Carry off-board bailout cylinder
No Set-point switch – Manual control of PO2 – 20 Minutes
Semi-closed for 12 Minutes
Flood recovery (dynamic)
Solenoid failure in the closed position (change setpoint to 0.5 and use manual oxygen addition to maintain desired setpoint)
Solenoid failure in the open position (reset setpoint to 1.3, maintain 1.1 via oxygen valve) (dynamic)
Out of gas (gas sharing by using buddies stage and hand off of stage)
Safety Stop (dynamic – if conditions permit)

## Slide 126: CCR Student Skills OW Dive 6 Do Each of the Following Drills at Least Once
Bailout cylinder removal and replacement if carried as stage
Manual control of PO2 for duration of the dive
Partial flood recovery
Hyperoxia Drill
Hypoxia Drill
Solenoid Failure in Closed Position Drill
Solenoid Failure in Open Position Drill
Hypercapnia
SMB Deployment
Ascend (without ascent line if conditions permit)

## Slide 127: CCR Student Skills OW Dive 7 - Student Reacts To Scenarios Do Each of the Following Drills at Least Once
Bailout cylinder removal and replacement if carried as stage
Inhalation counterlung inflating
Feeling unusual
Buoyancy changed to negative
Difficult breathing counterlung at correct volume
Weakness in legs
Shortness of breath
Nausea
Ears ringing
Hearing or visual abnormalities
You feel dizzy
Extreme quietness (absence of solenoid noise)
Solenoid fires but no oxygen injected

## Slide 128: CCR Student Skills OW Dive 8 Student Reacts To Scenarios Do Each of the Following Drills at Least Once
Extreme quietness (absence of solenoid noise)
Solenoid fires no oxygen injected
Diluent not being added
2 cells read high but low cell checks with Diluent PO2
2 cells read high and check with Diluent PO2
Shortness of breath
Feeling of well being
Feel like you are about to blackout
Hearing or visual abnormalities
You feel dizzy