## Slide 1
© IAND, Inc. dba IANTD 1985-2017.
All Rights Reserved
1
Professional Diver Education
IANTD Leading The Way Since 1985
International Association of Nitrox & Technical Divers

## Slide 2: Introductions
Speaker introduction (s)
Introduction of each person
  Name
  Diving experience
  Your expectation by the end of this course
2

## Slide 3: Ground Rules
There is NO SUCH THING as a silly question
There are no bad ideas
We will endeavor to start and end on time
Full attendance at all classes is required (unless otherwise arranged)
Assessment at the end
Certification issued if earned
3

## Slide 4: To get the MOST from the course
Focus on learning this material (not on what is happening at work or in your life currently)
Be active
  Ask questions
  Participate in discussions
  Take notes
  STOP me if you think I am going too fast or if you have a question.
4

## Slide 5: Housekeeping
Safety
  Building exits / emergency plans
Location of rest rooms
Parking
Liability releases
Medical Eligibility Forms
IANTD membership (optional)
Course fees
Cell phone - off please!
5

## Slide 6: Course Overview
I will now go over the schedule with you so we understand where and when we need to be.
  Academic Requirements
  Land drills
  Confined water training
  Open Water dives
6
Students demonstrating unsafe diving practices or unsafe attitudes will not be certified!

## Slide 7: Advice
The sport of SCUBA diving has many hazards:
  From the first time you put a regulator in your mouth and descended below the surface of the water you began accepting the risk that one of these hazards might seriously injure or even kill you.
  As your skills and experience progressed beyond that of an entry-level diver, you began choosing to make more advanced dives, and accepted the greater risks that went with them.
  In the IANTD X-CCR diver class, where exposure to diving environments are part of the curriculum, the risks are relevant.
7

## Slide 8: Learning Objective
It is intended that this course enhance participants knowledge and familiarity of Closed Circuit Rebreather Diving and expose divers to concerns when dealing with normal diving environments. By the end of this lecture and practical session you will be diving these configurations more safely and with greater enjoyment.
Your participation in this course should be part of a seasoned, carefully planned and informed progression.
8

## Slide 9: Prerequisites
Minimum 18 years of age
Certified as IANTD Advanced Nitrox Diver or Advanced Recreational Trimix (may be taken in conjunction with Instructor approval), or equivalent
9

## Slide 10: Certification Limitations
Diver qualified on specific rebreather
  X-CCR Closed Circuit Rebreather
Diver qualified within the sport diving depth and time limits
  Depth 140 fsw (42 msw) for Advanced EANx qualified
  Depth 160 fsw (48 msw) for Advanced Recreational Trimix qualified
  Decompression stop time not greater than 15 minutes
10
Training is purchased, certification is earned!

## Slide 11: Program Content
Minimum 500 minutes of confined and open water dive time
At least 6 open water dives
  Three (3) dives must be a minimum of 50 fsw (15 msw) and one (1) of these dives must be a minimum of 100 fsw (30 msw)
  Divers crossing over from SCR to CCR with 20 dives must:
    Complete 420 minutes of confined and open water time and 6 dives
11

## Slide 12: Program Content
  From one CCR to another CCR with 12 dives must:
    Have a CCR dive within the last 45 days
    Complete 60 min confined water and 180 minutes of water training with at least three (3) OW dives
X-CCR specific exam
  Minimum score of 80% with 100% remediation of missed questions
  Water Skills evaluation minimum score of 80%
    Theory and practical review to make studuent knowledgeable of mistakes on exam and water skills
12

## Slide 13: Equipment
IANTD S Drill check sheet C
X-CCR CCR
  Bailout cylinder (off board)
  required on all dives
  At depth, the maximum PO2 of
  gas in diluent cylinder should
  be 1.0 – 1.1 ATA
  This will allow for an adequate
  diluent flush
13

## Slide 14: Equipment
Exposure suit suitable for the environment
Back up dive tables
Slate and pencil
Reel and marker buoy
Depth gauge and timer
Knife, Z-cutter or shears
Mask and fins
14

## Slide 15: CCR – Mixed Gas
Gas mixed electronically
Virtually unlimited depth capabilities
Very efficient gas supply usage
PO2 setpoint or continuous oxygen flow
Less expensive to dive especially when used with helium based gases
15

## Slide 16: CCR & Partial Pressures
Electronic control system maintains constant PO2 setpoint
Oxygen sensors detect PO2 drop & trigger solenoid valve to inject additional oxygen
Remainder of gas in loop is the Diluent which could consist of one or more inert gases
16

## Slide 17: Rebreather History
Early and Recent History
17

## Slide 18: The British Influence ….. SCR
18
1878
1914

## Slide 19: The German Influence …... CCR
1911 – 1914
1941 – 1954
19

## Slide 20: Commercial & Scientific Use
In the 60's and 70's rebreathers are increasingly used for commercial saturation bail-out systems.
20

## Slide 21: Early History
17th Century - First conceived by Giovanni Borelli
1878 - First practical system produced by Henry Fleuss
1881 - First CO2 absorbent used by Khotinsky and Lake
Prior to WWI - Dräger produced systems
WWII - Italian & British Navies used Oxygen and Nitrox systems
21

## Slide 22: Recent History
1969 - Electrolung - first practical electronic control Rebreather
Biomarine CCR1000, Carleton Technologies Mk 15/16
Dräger Atlantis 1 1995, Dräger Dolphin in 1998 & DrägerRay in 1999
Cis-Lunar, Inspiration, CCR 2000, Megaladon, Prism Topaz, O2ptima & Evolution
Robust & affordable systems are now available
22

## Slide 23: Re-circulating Scuba
Gas supply
Gas control mechanism
Counterlung
CO2 removal system
Bail-out system
23
Photo: Matthew Addison

## Slide 24: General Design
24
Diagram od X-CCR

## Slide 25: General Design
24
Overview

## Slide 26: General Design
24
BM-CL configuration
FM-CL configuration

## Slide 27: Rules For Safe CCR Diving
Avoid complacency
Avoid distraction
Be a disciplined diver
Be a thinking diver
As the slogan goes always know your PO2
Do not be cheap
Make the CCR your primary diving equipment.
Practice bailout options periodically, assume that any mechanical or electrical device will fail
Accept all emergencies taught during training will happen
Do not start dives with a known system failure
25

## Slide 28: X-CCR Technical Data
Tanks change to appropriate
  Gas tanks optionally from 2L to 7L
  Quick release fasteners for easy and quick tank replacement
26

## Slide 29: X-CCR Technical Data
Radial scrubber:
  3.3 kg (7,4 lbs) CO2 absorbent basket
  Use Sofnolime 797, 1 - 2,5mm
  Optional smaller scrubber available
27
Use assembly checklist
in the user manual
Photo: Matthew Addison

## Slide 30: X-CCR Technical Data
The radial scrubber assembled
28

## Slide 31: X-CCR Technical Data
Loop
  Back-mounted or Front-mounted Counterlungs
  Click Lock Couples on every breathing loop connection point
  Bail-Out Valve (BOV)
  One way mushroom valves in the BOV ➜ Gas flow direction
  ADV (Automatic Diluent Valve) integrated into T-piece
  Shut-Off Valve (at ADV)
29

## Slide 32: X-CCR Technical Data
Head
  Quick bayonet lock
  Shearwater controller
  HUD
  Flexible secondary
  High pressure sensors
  CO2 solid state sensor
  Sensor cartridge
  Separete Li-Ion accu 18650
    one for solenoid
    one for HUD
30
Photo: Matthew Addison

## Slide 33: X-CCR Technical Data
Flexible Connection of controlling and monitoring devices
30

## Slide 34: X-CCR Technical Data
O2 sensors
  Easy removable and swappable sensor cartridge
31
Photo: Matthew Addison
  3 O2 sensors
  O2 sensor should be replaced after one year or after 18 month from its manufacturing date
  NaNS01 Coaxial
CO2 sensor
  One CO2 sensor
  Solid state

## Slide 35: X-CCR Technical Data
Solenoid
  Upstream valve
  Made of AISI 316L
  Rated for up to 17 bar
  With built in O2 filter in the fitting
  Pre-scrubber O2 injection
32

## Slide 36: X-CCR Technical Data
Main Body
  Robust aluminum or optionaly derlin canister
  Quick release fasteners for easy replacement of gas cylinders
  Gas cylinders optionally from 2L to 7L
  Diluent manifold with up to 8 outlets
  Oxygen manifold with up to 5 outlets
  Back-plate adapter
33

## Slide 37: X-CCR Technical Data
Apeks regulators
  Intermediate pressure
    9.5 to 10.5 bar oxygen regulator
    9.5 to 10.5 bar diluent regulator
Oxygen and diluent MAV (manual add
valve) can also be used to
plug in offboard gas
34

## Slide 38: X-CCR Technical Data
Head-Up Display LED signals
  Uses Smither’s analog code showing PPO2 reading of each sensor.
  Flashes yellow over green at pO2 1.0
  Flashes one green for each 0.1 above 1.0
  Flashes one yellow for each 0.1 below 1.0
  Flashes multiple reds for pO2 > 1.6 or < 0.4
35
Photo: Matthew Addison

## Slide 39: Calibration
Use Oxy Calibration Kit
36
Oxygen only fills chamber of sensors to save gas
Shearwater controller calibration
HUD calibration
Secondary calibration

## Slide 40: X-CCR – Doing the Math
Checking the linearity of the O2 sensors
  Linearity is checked to see if the output of the cell will track the O2 increase in a linear fashion (no "humps" or "valleys" of mV output) from 21% to 100% O2
Checking O2 sensors for current limiting
  Current limiting is done either in a pressure pot or at a depth sufficient to increase a pure O2 loop to a PPO2 to 1.6
  This is critical as cells get old they will not read high resulting is extremely dangerous diving situations
37

## Slide 41: X-CCR – Doing the Math
  Mathematically we can determine what the mV reading should be when the loop is flooded with 100% O2
    1.0 atm/0.21 atm = 4.76
    i.e.: S1 – 8.3 mV, S2 – 10.1 mV, S3 – 9.5 mV on air
    So mV on 100% O2 should be:
      i.e.: S1 – 8.3 x 4.76 = 39.5 mV, S2 – 10.1 x 4.76 = 48 mV, S3 – 9.5 x 4.76 = 45.2
38

## Slide 42: X-CCR – Oxygen Cells
As oxygen cells age, their current output will slowly decrease. Because of this aging, it is necessary to verify calibration, or re-calibrate prior to use.
X-CCR recommends replacing oxygen sensors one year from their stamped date
39
Calibration is extremely easy and is performed on the assembled unit

## Slide 43: Electrical Oxygen Sensors
Critical components - redundancy
Galvanic fuel cells
Lead anode - gold plated cathode - Potassium Hydroxide solution
Lead is oxidized producing small current between anode & cathode
Individually calibrated
Affected by humidity and temperature
40

## Slide 44: X-CCR – Interpreting PO2
The PO2’s from the 3 Oxygen Cells are the most important data you have to monitor
Compare the PO2 displays to each other
Note the speed at which the PO2 changes
41
Check your PPO2 once every minute!

## Slide 45: Cylinder Considerations
BCD & drysuit inflation gas will affect Rebreather duration
Diluent used primarily during descents
Oxygen is more likely to limit dive duration
42

## Slide 46: The Counterlung
Necessary for free breathing
  Empty bottle vs. paper bag
Constant Buoyancy
  Exhale: lung volume decreased & bag volume increases
  Inhale: lung volume increases & bag volume decreases
  Compare to Open Circuit Scuba
Position to minimize pressure differential between lungs and counterlung
43

## Slide 47: Hydrostatic Effect
Chest mounted bag - diver horizontal
  Inhale less effort
  Exhale more effort
Back mounted bag - diver horizontal
  Inhale more effort
  Exhale less effort
Shoulder mounted bags - most positions
  Inhale & exhale equal effort
44

## Slide 48: Breathing Loop
Scrubber for CO2 Removal
  Exhaled gas passes through this for “filtering effect”
  Efficiency and work of breathing is related to size / types of granules
  Temperature sensitive
  Design also effects the efficiency
45

## Slide 49: Absorbent Canister Design
Gas exposed to sufficient surface area of absorbent to remove CO2
Gas flow rate across absorbent sufficient time (dwell time) for chemical removal of CO2
Simple & correct packing to prevent ‘channeling’ of absorbent
Prevent excess moisture from reaching absorbent
46

## Slide 50: Absorbent Canister
Flow System – Radial scrubber
47

## Slide 51: Absorbent Types
Barium Hydroxide - the earliest form of absorbent used
Lithium Hydroxide - long lasting and efficient, but must be carefully handled and is expensive
Soda Lime - a commonly used absorbent available under trade names such as Sofnolime™
48
All Absorbents will Produce a
Caustic Solution When Mixed with Water!!!

## Slide 52: Carbon Dioxide Absorption
Typical diving grade soda lime absorbent
  94% Calcium Hydroxide [Ca(OH)2]
  4% Sodium Hydroxide [NaOH]
  <1% Silica (binding agent)
Some types change color with use
Slightly hydrated to ensure production of Carbonic Acid
49

## Slide 53: Carbon Dioxide Absorption
CO2 reacts with water (vapor) to form weak Carbonic Acid
Carbonic Acid reacts with base to produce salt (chalk), water & heat
50
CO2 + H2O ⇨ H2CO3
H2CO3 + 2NaOH ⇨ Na2CO3 + 2H2O + Heat
H2CO3 + Ca(OH)2 ⇨ CaCO3 + 2H2O + Heat

## Slide 54: CO2 Absorbent - Duration Variables
Chemical composition
Canister Design
Canister volume
Temperature
Exertion level
Moisture content
51

## Slide 55: CO2 Absorbent - Materials
X-CCR Scrubber
  Tested under CE conditions
    CO2 production 1.6 liters/min
    Water temperature 4 degrees Celcius
    RMV 40 liter/min
  Standard scrubber
    Duration 5 hours at 100 meters
52

## Slide 56: Face Masks
Rebreathers have limited gas supply
Proper fitting mask to prevent leaks
Repeated mask clearing depletes gas supply
53

## Slide 57: Breathing Characteristics
More natural breathing than Open Circuit
Breathing resistance depends on location of counterlung and diver’s body position
Water in loop increases breathing resistance
Humid gas reduces dehydration of diver
Warm gas reduces heat loss from diver
Both effects should reduce the risk of DCS
54

## Slide 58: Pre-Dive and set up
Complete X-CCR assembly user manual
  Your instructor will follow you through this procedure
  Check off each item in pre dive set up of X-CCR
  Follow the post dive procedures in X-CCR manual
  Refer to and use the maintance log sheet as needed
55

## Slide 59: Pre-Dive and set up
Follow both the predive on the check list and the IANTD S drill chart
This can be done at same time
Note The IANTD S drill requires each buddy verifies the other completes the process
56

## Slide 60: Pre-Dive
Let us break away from this power point and work with our IANTD C-3401 S Drill Chart
57

## Slide 61: Pre-dive Breathe Sequence
Pre-dive breathe for 5 minutes
    Confirm bail-out system operation
    Confirm cylinders on
    Confirm solenoid is keeping pO2 at setpoint
    Operate O2 manual addition valves
    Confirm O2 and Diluent pressure gauges
    Confirm BCD inflation and deflation
    Confirm ADV operation
58

## Slide 62: Dive Procedures
Initial in-water verification
Descent - diluent addition
Buoyancy control
Monitoring PO2
Minimum loop volume
Monitoring gas supplies
Ascents
59

## Slide 63: Initial In-Water Verification
Check for leaks
Verify PO2 display working
Adjust buoyancy
Check your dive buddy
60

## Slide 64: Descents
Counterlung collapses as ambient pressure increases
  Add diluent to maintain breathing volume
Compensation by diluent gas addition
Rapid descents cause PO2 spikes
Enter the water with PO2 setpoint of 0.7
Once at depth adjust PO2 to desired setpoint
61

## Slide 65: Buoyancy Control
No buoyancy changes during breathing cycle
  Except for oxygen metabolised
Buoyancy adjustments using lung volume therefore not feasible
Counterlung collapses during descent & expands during ascent
Buoyancy change from fully collapsed to fully inflated is considerable
62

## Slide 66: Monitoring PO2
Hypoxia & Hyperoxia are real dangers
Frequent cross checking of both primary & secondary
63
Constant PO2 Monitoring is Vital
Check every 1 minute

## Slide 67: Monitoring Gas Supplies
Gas supplies used at much slower rate than OC but monitoring is still necessary
Small gas supply quickly used if there are leaks in the loop, frequent mask clearing or frequent ascents / descents
O2 supply not diluent supply, typically limits duration of dive
64

## Slide 68: Ascents
Buoyancy changes due to expansion of the counterlung, BCD, and drysuit
PO2 should not be allowed to drop
Oxygen can be manually added as necessary
65

## Slide 69: Physiological Concerns
Hypoxia (O2 deficiency)
Hyperoxia (CNS O2 toxicity)
Hypercapnia (CO2 toxicity)
Decompression Sickness
Chemical Injury
66
Hypoxia, Hyperoxia & Hypercapnia may cause Loss of Consciousness with little or No warning!

## Slide 70: Failure Modes
Bail-out Scenarios
  Hypoxia
  Hyperoxia
  Hypercapnia
  Complete electronics failure
    Semi-closed mode
    Minimum loop volume
67
In an Emergency
Poorly Learned Survival Skills Are Lost First!

## Slide 71: Hypoxia
Lack of oxygen at cellular level
  First signs at PO2 of 0.16
  Serious signs at PO2 of 0.10
Lack of coordination
  Confusion, euphoria, inability to think clearly, unconsciousness & death
68
Hypoxia Can Lead to
Unconsciousness & Death Without Warning

## Slide 72: Hypoxia
Procedure
  Switch to Open Circuit for one or more sanity breaths
  Switch back to Rebreather
  Diluent flush
  Check PO2
  Manually add oxygen to desired PO2
  Repeat until PO2 setpoint is obtained
69
If PO2 Remains Low, Switch to Open Circuit & Bail-Out
Hypoxia Can Lead to
Unconsciousness & Death Without Warning

## Slide 73: Hypoxia
Problems that lead to Hypoxia:
  Failure to turn oxygen on
  Manual add valve screen blocked with salt or debris
  Wrong gas in oxygen cylinder
  Failure to calibrate
  Failure to do pre dive Breathe and checks
  Failure to monitor PO2
  Running out of oxygen supply gas
70
Mistakes Due To Complacency or Distraction = Accidents or Death

## Slide 74: Hyperoxia
Excess of oxygen at cellular level
PO2 of 0.5 to 1.0 ATA/Bar
  Whole Body Oxygen Toxicity
PO2 > 1.0 ATA/Bar
  CNS Oxygen Toxicity
Convulsions underwater may result in drowning
71
Hyperoxia Can Lead to
Convulsion & Drowning Without Warning

## Slide 75: Hyperoxia
Procedure
  If well above set point switch to Open-Circuit for one or more sanity breaths
    If slightly above set point simply flush loop to bring down
  Switch back to Rebreather
  Diluent flush
  Check PO2
  Repeat until PO2 setpoint is obtained
72
Hyperoxia Can Lead to
Convulsion & Drowning Without Warning
If PO2 Remains High, Switch to Open Circuit & Bail-Out

## Slide 76: CNS Oxygen Toxicity
Signs & Symptoms
73
CON | Convulsions
V | Vision
E | Ears, hearing disturbances
N | Nausea
T | Twitching
I | Irritability
D | Dizziness

## Slide 77: Tracking O2 Limits
CNS tracking couldn’t be simpler
Use the IANTD O2 exposure table, at 1.3 ATA you have 3 hours dive time or 3.5 hours/day
Remember, if you push the PO2 up to 1.4 ATA the dive time is reduced to 2.5 hours or 3 hours per day
74
Refer to IANTD OTU /CNS Tracking Table C 3201 in the student kit to determine exact oxygen exposure.
Then for repetitive CNS value use the oxygen surface credit chart.

## Slide 78: Problems that lead to Hyperoxia
High percentage of O2 in diluent
Solenoid stuck open
Rapid descent started with to high of a setpoint
Adding oxygen during descent
Setpoint maintained too high for dive duration thus exceeding oxygen clock
Failure to calibrate unit
75

## Slide 79: Hypercapnia
PCO2
  0.03 ATA/Bar – doubles breathing rate (dyspnea)
  0.06 ATA/Bar – distress, confusion, lack of coordination
  0.10 ATA/Bar – severe mental impairment
  0.12 ATA/Bar – loss of consciousness, death
76
Hypercapnia Can Lead to
Unconsciouness & Death Without Warning

## Slide 80: Hypercapnia
Bailout to OC
Ascend
77
Hypercapnia Can Lead to
Unconsciouness & Death Without Warning

## Slide 81: Hypercapnia
Problems that lead to hypercapnia
  Using canister beyond it’s rated /actual duration
  Canister over-breathing
  Wrong material
  Using absorbent that has exceed it’s expiration date
  Absorbent is wet
  Deep diving on partially used canister
78

## Slide 82: CO2 Absorbent Problems
Flooded Canister
  CO2 absorption fails, caustic cocktail in loop
Absorbent Failure
  CO2 absorption fails
79
Switch to Open Circuit Bail-Out
Switch to Open Circuit Bail-Out

## Slide 83: Moisture In Loop
Always some moisture due to condensation
Accidental removal of mouthpiece
Move water into exhale counterlung
80

## Slide 84: Water In Loop
Leaky hose connections, damaged hoses, punctured counterlung & other damaged loop components
Gurgling sound & breathing resistance
Decrease in buoyancy
Clear flooded loop
If problem continues
81
Switch to Open Circuit Bail-Out

## Slide 85: Asphyxia
If diver breathes in and out of a closed bag
  CO2 rises and O2 falls
Dyspnea - increasing shortness of breath
Breathing difficulties caused by increased CO2
Death caused by insufficient O2
82

## Slide 86: Complete Electronics Failure
Extreme Emergency - Diver Chooses To Continue Diving Rebreather
  With proper training beyond scope of this course, diver has three options
    Open Circuit bail-out
    Semi-Closed mode
    Minimum Loop Volume while at constant depth
83
IANTD Recommends Open Circuit Bail-Out

## Slide 87: External Boom Scenario
Can be classified as gas that is being lost to the environment and not into the loop.
Such loses can include:
  LP or HP hose failures
  Regulator failures
  Tank o-ring extrusions or burst disk failures
84
IANTD Recommends Open Circuit Bail-Out

## Slide 88: External Boom Scenario
Procedure
  Turn off both gas supply cylinders
  Look at the diluent and oxygen SPG
  Check PO2
  Determine which side has failed and what the failure is
  Open the valve of the side that has not failed and abort the dive in either CCR mode or end in OC mode.
85
IANTD Recommends Open Circuit Bail-Out

## Slide 89: Internal Boom Scenario
A failure that leads to gas being added to the loop.
These may include the:
  ADV failing in the open position
  Manual oxygen add valve failing open.
  Solenoid stuck in open position
86
IANTD Recommends Open Circuit Bail-Out

## Slide 90: Internal Boom Scenario
Indictors are more subtle:
  Increase in buoyancy
  Chipmunk cheeks
  Increased breathing resistance especially on exhalation
  The sound of gas moving
  Increased or decreased PO2.
87
IANTD Recommends Open Circuit Bail-Out

## Slide 91: Internal Boom Scenario
Procedure
  Turn off both gas supply cylinders
  Look at the diluent and oxygen SPG
  Check PO2
  Determine which side has failed and what the failure is
  Open the valve of the side that has not failed and abort the dive in either CCR mode or end in OC mode.
88
IANTD Recommends Open Circuit Bail-Out

## Slide 92: O2 Sensor Failure
During the dive one or more O2 sensors can fail
The Shearwater contrtoller will vote out the sensor(s) out of the range
The best O2 sensor might be voted out
A validation procedure is needed – Diluent flush!
89
IANTD Recommends Open Circuit Bail-Out

## Slide 93: O2 Sensor Failure
Validation procedure
  Do a diluent flush
  Compare the 3 O2 sensors values with the PPO2 of the diluent at actual depth
  If the sensor was voted out correctly:
    Follow Shearwater and abort/turn the dive
  If the sensor voted out was incorrectly:
    Abort/turn the dive using the O2 sensor voted out as parameter of your PO2
90
IANTD Recommends Open Circuit Bail-Out

## Slide 94: Basic Respiratory Physiology
21% oxygen in air at sea level
4% absorbed into blood
  Exhaled air contains approximately 17% O2
Urge to breathe is triggered by PCO2
Respiratory rate determined by rate of CO2 production
91

## Slide 95: Basic Respiratory Physiology
Respiratory minute volume (RMV) = total gas ventilated in one minute
  RMV determined by respiratory rate & volume of gas ventilated each breath
OC duration determined by RMV
SCR duration determined by flow rate
CCR duration determined by O2 metabolic rate
92

## Slide 96: Oxygen Metabolism
93
Oxygen Consumption Varies With Work Load | 
At rest | 0.3 to 0.5 l/m
Light to moderate work | 1.0 to 1.5 l/m
Heavy work | 2.0 to 2.5 l/m
Maximum work | 3.0 to 3.5 l/m
Increase Gas Efficiency by Rebreathing It!

## Slide 97: Gas Consumption Comparison
Depth (fsw) | Depth (msw) | Absolute Pressure ATA/BAr | OC lpm | CCR lpm
0 | 0 | 1.0 | 26 | 1
33 | 10 | 2.0 | 50 | 1
66 | 20 | 3.0 | 75 | 1
99 | 30 | 4.0 | 100 | 1
132 | 40 | 5.0 | 125 | 1
165 | 50 | 6.0 | 150 | 1
231 | 70 | 8.0 | 200 | 1
297 | 90 | 10.0 | 250 | 1
94

## Slide 98: Closed Circuit Oxygen Metabolism
O2 supply = 3 liters @ 200 Bar = 600 litres
Metabolic rate = 1.0 lpm @ moderate work load
95
Assumes no leakage from mask or loop. Duration independent of depth.

## Slide 99: Open Circuit Gas Usage
X-CCR : 3 litres at 200 Bar = 600 litres
Open Circuit Equipment:
  RMV at surface = 20 lpm
  RMV at 66 fsw (20 msw) = 60 lpm
  600 litres/60 litres per minute = 10 minutes
96
10 min Open Circuit = 10 hours on JJ-CCR

## Slide 100: Rebreathers & Decompression
Partial pressure of inert gas determines decompression obligation
Open Circuit & Semi-Closed Circuit
  PO2 maximum only at target depth
With Closed Circuit constant PO2 (setpoint) increases decompression efficiency
Dramatically reduces decompression obligation
97

## Slide 101: Decompression Efficiency
The most efficient is Closed Circuit Rebreather
The second most efficient is EANx or Trimix Open Circuit
The third is Semi-Closed Rebreather
The least efficient is Air Open Circuit
98
CCR is the ideal system for decompression
efficiency and ease of oxygen tracking

## Slide 102: Breathing Gas
Oxygen & Inert Gas % -- Note: X-CCR recommends a high set point of 1.2
99
Depth (fsw) | Depth (msw) | Pressure (Bar) | PO2 (Bar) | FO2 | FInert
10 | 3 | 1.3 | 1.3 | 100% | 0%
20 | 6 | 1.6 | 1.3 | 81.3% | 19.7%
33 | 10 | 2.0 | 1.3 | 65.0% | 35%
66 | 20 | 3.0 | 1.3 | 43.3% | 56.7%
99 | 30 | 4.0 | 1.3 | 32.5% | 67.5%
132 | 40 | 5.0 | 1.3 | 26.0% | 74.0%
165 | 50 | 6.0 | 1.3 | 21.7% | 78.3%

## Slide 103: CCR Buddies
CCR Buddy with X-CCR
  Walk through each other configuration to increase safety
CCR Buddy with a CCR other than X-CCR
  If certified as diver on the buddy CCR, just walkthrough each other configuration to increase safety
100

## Slide 104: CCR Buddies
  If not certified as diver on the buddy CCR, get to know HOW:
    To close the BOV
    To switch setpoint
    To Switch to OC
    To add O2 and Diluent manually
101

## Slide 105: CCR Buddies
OC Buddy
  Explain that:
    If possible CCR Divers prefers to go around than over the obstacles
    During descent and ascent, CCR Divers have other things to take care
    If he runs out of gas, from which tank he can breathe and how
  Explain HOW:
    To close the BOV
    To switch setpoint
    To switch to OC
    To add O2 and Diluent manually
102

## Slide 106: CCR Buddies
    To interpreted the HUD lights
    You want to be rescue in an emergency
    To do a buddy breathe, in case both divers need to share the bailout gas (Rare but…)
  Walkthrough each other configuration to increase safety
103

## Slide 107: Chemical Injury
Caustic cocktail
  May produce mild irritation to third degree chemical burns
  Some absorbents may be lethal if wet (Lithium Hydroxide for instance)
Battery related injuries
Electrical injury
104

## Slide 108: Rebreather Maintenance
Disinfecting & cleaning
O-rings
Hoses
Counterlungs
Scrubber Basket
105

## Slide 109: After Each Day Of Diving
Vent O2 sensors to the atmosphere
Let the sensor head dry out
Drain exhale counterlung
Sterilize the full breathing loop after each day of use
Re-pack absorbent, fill cylinder as necessary
106

## Slide 110: Post Dive & Storage
Rinse exterior of unit
Remove/dispose absorbent
Clean scrubber canister
Rinse/disinfect counterlungs & hoses
For storage, leave cylinder partially filled
Allow unit to dry, lubricate all O-rings
107

## Slide 111: O-Rings
Do not disturb O-rings unnecessarily
Carefully inspect prior to reassembly
Replace damaged O-rings
Excessive lubrication not required
Check O-ring grooves for damage
O2 compatible lubricants only
Factory sealed compartments - don’t tamper
108

## Slide 112: Hoses
Check for visible damage after every dive
Store in hard carry case
Do not carry unit by hoses
Do not place heavy equipment on hoses
109

## Slide 113: Counterlungs
Check loop interface ports for damage to threads, etc.
Keep dry (vented) when not in use
110

## Slide 114: Summary
Advantages of Rebreathers greatly outweigh the disadvantages
Correct training is obligatory
The X-CCR is a safe and effective means of CCR diving
111
Always Know Your PO2
Be Sensible, Be Safe!

## Slide 115
Do you have any questions for me?
Would you please fill in a course critique?
Let’s go DIVING!
112